## Slide 1: Pseudo LIDAR

## Slide 2: What is LIDAR?
Based on time of flight (time it takes light to go out, bounce off and object and come back). Returns 3D coordinates relative to the sensor.

## Slide 3: 3D Object detection

## Slide 4: Stereo vs. lidar
(Tesla vs. Waymo)

## Slide 6: LiDAR Pipeline
Deep Object Detection
LiDAR point cloud
Frontal Image(s)
Predicted B-Boxes
[Ku. et al. 2018, Yang et al. 2018, Shi et al. 2019]

## Slide 7: Stereo Pipeline
Stereo Images
Disparity Estimation
Disparity Map
Stereo Images
+ Depth Map
Deep Object Detection
Predicted B-Boxes
[Chen et al. 2018]

## Slide 8: 3D object detectioN (Acc.)
Chart: 
| Easy | Moderate | Hard
Stereo [Chen et al. 15] | 12.6 | 9.4 | 7.6
Lidar [Xu et al. 18] | 87.8 | 86 | 85.8
KITTI benchmark [Geiger et al. 2013] (Average Precision Bird-Eye-View)
Chart: 
| Easy | Moderate | Hard
Stereo [Chen et al. 15] | 55 | 41 | 35
Lidar [Xu et al. 18] | 96 | 90 | 87
IoU=0.5
IoU=0.7

## Slide 9: Depth map

## Slide 10: Point cloud

## Slide 11: Point cloud

## Slide 12: Filters on depth maps

## Slide 13: Filters on depth maps

## Slide 14: conjecture
Frontal Depth Maps are ill suited for ConvNets
Convert to Bird-Eye-View first!

## Slide 15: Pseudo-LiDar Pipeline
Stereo Images
Disparity Estimation
Deep Object Detection
Frontal Image(s)
Predicted B-Boxes
Pseudo-Lidar (Voxels)
Disparity Map

## Slide 16: 3D object detection (Acc.)
Chart: 
| Easy | Moderate | Hard
Stereo [Chen et al. 15] | 12.6 | 9.4 | 7.6
Stereo (pseudo Lidar) | 0 | 0 | 0
Lidar [Xu et al. 18] | 87.8 | 86 | 85.8
Chart: 
| Easy | Moderate | Hard
Stereo [Chen et al. 15] | 55 | 41 | 35
Stereo (pseudo Lidar) | 0 | 0 | 0
Lidar [Xu et al. 18] | 96 | 90 | 87
IoU=0.5
IoU=0.7
KITTI benchmark [Geiger et al. 2013] (Average Precision Bird-Eye-View)

## Slide 17: 3D object detection (Acc.)
Chart: 
| Easy | Moderate | Hard
Stereo [Chen et al. 15] | 12.6 | 9.4 | 7.6
Stereo (pseudo Lidar) | 73.4 | 56 | 49
Lidar [Xu et al. 18] | 87.8 | 86 | 85.8
Chart: 
| Easy | Moderate | Hard
Stereo [Chen et al. 15] | 55 | 41 | 35
Stereo (pseudo Lidar) | 89 | 76 | 67
Lidar [Xu et al. 18] | 96 | 90 | 87
IoU=0.5
IoU=0.7
KITTI benchmark [Geiger et al. 2013] (Average Precision Bird-Eye-View)

## Slide 19: DisparitY
Stereo Images
Disparity Estimation
Disparity Map

## Slide 20
disparity
width
height

## Slide 21
4D convolution
softmax
disparity map

## Slide 22: Disparity vs depth
Chart: 
| 0-10 | 10-20 | 20-30 | 30-40 | 40-50 | 50-60 | 60-70
Disparity Net | 0.04 | 0.11 | 0.35 | 0.83 | 1.2 | 2 | 2.4
Median error in meters
distance in meters

## Slide 23: Stereo Depth Network
Stereo Images
Disparity Cube
Depth Cube
resolution
1 pixel
resolution
1 m
interpolation
softmax
Depth Map
L1-loss on depth

## Slide 24: Stereo Depth Network
Depth Cube
depth
(1m)
width
height
softmax
Depth Map
L1-loss on depth

## Slide 25: Disparity vs depth
Chart: 
| 0-10 | 10-20 | 20-30 | 30-40 | 40-50 | 50-60 | 60-70
Disparity Net | 0.04 | 0.11 | 0.35 | 0.83 | 1.2 | 2 | 2.4
Depth Net | 0.06 | 0.12 | 0.3 | 0.6 | 0.89 | 1.32 | 1.73
Median error in meters
distance in meters

## Slide 26
Locally Linear Depth Correction
from (cheap) 4-beam LiDAR signal*
*(we downsampled 64 KITTI beams to 4 beams)

## Slide 27
4-Beam LiDAR
pseudo-LiDAR

## Slide 28: 3D object detectioN (Acc.)
Chart: 
| Easy | Moderate | Hard
Stereo [Chen et al. 15] | 13 | 9.4 | 7.6
Stereo (pseudo Lidar DepthNet) | 82 | 64 | 57
pseudo-Lidar++ | 87 | 77 | 73
Lidar 64 beam [Xu et al. 18] | 88 | 86 | 86
KITTI benchmark [Geiger et al. 2013]
Chart: 
| Easy | Moderate | Hard
Stereo [Chen et al. 15] | 55 | 41 | 35
Stereo (pseudo Lidar) | 90 | 84 | 77
pseudo-Lidar++ | 95 | 87.5 | 84.4
Lidar [Xu et al. 18] | 96 | 90 | 87
IoU=0.5
IoU=0.7

## Slide 30: What advantages do stereo cameras have compared to expensive LiDAR sensors?
Cheaper hardware setup
Passive sensing (no emitter)
High spatial resolution possible
depth accuracy inversely proportional to distance

## Slide 31: What is monocular and stereo depth?
Monocular: depth from one image (how?)
Stereo: depth from two aligned views

## Slide 32: What are Siamese networks?
Twin networks sharing weights
Compare two inputs directly
Used for disparity estimation
Output: similarity or match score

## Slide 33: The authors mention they remove points higher than 1 meter above the vehicle. What is the benefit of this and what if there's an overpass or a truck higher than 1 meter that's actually important to detect?
Reduces noise from sky/trees
Focuses on drivable space
Improves detection consistency
Can miss tall objects like trucks

## Slide 34: How did the authors choose the ROI for BEV cropping?
They inherit this from the current LIDAR algorithms… (e.g. AVOD, Frustum PointNet), They have their own assumptions about the spatial region over which they operate

## Slide 35: Why does performance degrade sharply beyond 30 m, and can multi-scale fusion or hierarchical depth priors reduce that collapse?
Stereo depth error increases
Small objects occupy few pixels

## Slide 36: How would the system react to an optical illusion photo where a small nearby object looks like a large distant one? Would it misjudge the object’s depth or scale?

## Slide 37: So, is the main insight here that because LiDAR-based pipelines are the highest-performing, other forms of 3D data should be converted to LiDAR? Can we generalise and say that whenever a particular representation X is "default" or most developed, you can get further with a new representation Y by working on Y->X conversion rather than developing technology for Y from scratch?

## Slide 38: What would the implications of this gap be for self driving task activities such as material identification, occlusion inference, or mirror detection, and how would multimodal fusion work to fill these gaps?

## Slide 40: “Normalized Camera”
Pinhole at (0,0,0), point P at (X,Y,Z)
Virtual film at Z = 1 plane.
Point X,Y,Z is imaged at intersection of:
  Line from (0,0,0) to (X,Y,Z), and
  the Z = 1 plane
Intersection point (x,y), has coordinates
  (X/Z, Y/Z, 1)
This is called the “normalized camera model”
What happens when focal length is not 1?
Camera Center of Projection

## Slide 41
f
(X,Y,Z)
Z-axis
Image plane
Pinhole, (Center of projection), at (0,0,0)

## Slide 42: …but the cow is not a sphere
We don’t just want to know where, mathematically, the point ends up on the image plane… we want to know the pixel coordinates of the point.
Why might this be hard?!

## Slide 43: Intrinsic Camera Parameters
CCD sensor array
The pixels may be rectangular:
x = aX/Z
Y = bY/Z

## Slide 44: Intrinsic Camera Parameters
CCD sensor array
Chip not centered, or 0,0 may not be center of the chip.
x = aX/Z + x0
Y = bY/Z + y0

## Slide 45: Intrinsic Camera Parameters
cheap
glue
cheap CMOS chip
cheap lens
image
cheap camera
Ugly relationship between (X,Y,Z) and (x,y).
x = aX/Z – a cot(q) Y/Z + x0
y = b/sin(q) Y/Z + y0

## Slide 46: Homogeneous Coordinates
Represent 2d point using 3 numbers, instead of the usual 2 numbers.
Mapping 2d 2d homogeneous:
  (x,y)  (x,y,1)
  (x,y)  (sx, sy, s)
Mapping 2d homogeneous to 2d
  (a,b,w)  (a/w, b/w)
The coordinates of a 3D point (X,Y,Z) *already is* the 2D (but homogeneous) coordinates of its projection.
Will make some things simpler and linear.

## Slide 47: Why?!
x = aX/Z – a cot(q) Y/Z + x0
y = b/sin(q) Y/Z + y0

## Slide 48
1080 x 1920 (1920 heigh)
xo, yo = 540, 960
We see 8 meters wide at 10 m distance
1350 0 540 X
0 1350 960 Y
0 0 1 Z
Xf + 540Z
Yf + 960Z
Z
Xf/Z + 540
Yf/Z + 960
1
When X is -4, and Z is 10, I want x = 0 x = Xf/Z + 540
0 = -4f/10 + 540
4f/10 = 540
4f = 5400
f = 1350

## Slide 49: Homogenous Coordinates!
Equation of a line on the plane?
Equation of a plane through the origin in 3D?

## Slide 50
Given enough examples of 3D points and their 2D projections, we can solve for the 5 intrinsic parameters…
Example calibration object…

## Slide 51: Practical Linear Algebra 1:
Given many examples of the equation at the right, solve for the matrix of values fx, fy, s, x0, y0
How can we solve for this?

## Slide 52
Given enough examples of 3D points and their 2D projections, we can solve for the 5 intrinsic parameters…
… and all this assumes that we know X,Y,Z
(0,0,0)
Exactly Known!

## Slide 53
More commonly, we can put a collection of points (usually in a grid) in the world with known relative position, but with unknown position relative to the camera.
Then we need to solve for the intrinsic calibration parameters, and the extrinsic parameters (the unknown relative position of the grid).
How do we represent the unknown relative position of the grid?

## Slide 54
The grid defines its own coordinate system
X
Y
Z
That coordinate system has a
Euclidean transformation that relates its coordinates to the camera coordinates… that is, there is some R, T such that:
With enough example points, could we solve for R,T?

## Slide 55
An aside…Representation of Rotation with a Rotation Matrix
Rotation matrix R has two properties:
Property 1:
    R is orthonormal, i.e.
In other words,
Property 2: Determinant of R is 1.
Therefore, although the following matrix is orthonormal,
it is not a rotation matrix because its determinant is -1.
this is a reflection matrix

## Slide 56
Representation of Rotation -- Euler Angles
Euler angles
  pitch: rotation about x axis :
  yaw: rotation about y axis:
  roll: rotation about z axis:
X
Y
Z

## Slide 57
+
P is a 4X3 matrix, that defines projection of points (used in graphics). P has 11 degrees of freedom, (the scale of the matrix doesn’t matter). 5 intrinsic parameters, 3 rotation, 3 translation
Putting it all together…

## Slide 58
Given many examples of:
  World points (X,Y,Z), and
  Their image points (x,y)
Solve for P.
Then
translation
Rotation + intrinsic, all mixed up.

## Slide 59
Then take the QR decomposition of this part of the matrix to get the rotation and the intrinsic parameters.
(from mathworld).