## Slide 1: Lecture 08: Calibration and Pose Estimation
Slides inspired/borrowed from Steve Seitz and Rick Szeliski and Alexei Efros and James Hays and Linda Shapiro
Image from: https://developer.ridgerun.com/wiki/index.php?title=Full_Body_Pose_Estimation_for_Sports_Analysis_-_AprilTag_Camera_Calibration

## Slide 2: Image Mosaics
Can set scale factor i=1. So, there are 8 unkowns.
Set up a system of linear equations:
Ah = b
where vector of unknowns h = [a,b,c,d,e,f,g,h]T
Need at least 8 eqs, but the more the better…
Solve for h. If overconstrained, solve using least-squares:
Can be done in Matlab using “\” command
  see “help lmdivide”
p’ = Hp

## Slide 3: Today: Camera Calibration

## Slide 4: Today: Camera Calibration
No longer an image warp, translating 2D images to each other, but instead mapping 3D points to a 2D image. Main problem is to learn in this situation:

## Slide 5: Camera Calibration
A funny object with multiple planes.

## Slide 6: Camera calibration
Given n points with known 3D coordinates Xi and known image projections pi, estimate the camera parameters
Xi
pi
Slide credit: S. Lazebnik

## Slide 7: Today: Solve for the “Direct Linear Transformation”

## Slide 8: In reality: solve for projection matrix
Place a known object in the scene
  identify correspondence between image and scene
  compute mapping from scene to image

## Slide 9: Camera Calibration Targets
Using a tape measure
312.747 309.140 30.086
305.796 311.649 30.356
307.694 312.358 30.418
310.149 307.186 29.298
311.937 310.105 29.216
311.202 307.572 30.682
307.106 306.876 28.660
309.317 312.490 30.230
307.435 310.151 29.318
308.253 306.300 28.881
306.650 309.301 28.905
308.069 306.831 29.189
309.671 308.834 29.029
308.255 309.955 29.267
307.546 308.613 28.963
311.036 309.206 28.913
307.518 308.175 29.069
309.950 311.262 29.990
312.160 310.772 29.080
311.988 312.709 30.514
880 214
43 203
270 197
886 347
745 302
943 128
476 590
419 214
317 335
783 521
235 427
665 429
655 362
427 333
412 415
746 351
434 415
525 234
716 308
602 187
Known 3d locations
Known 2d image coords
Image credit: J. Hays

## Slide 10: Camera Calibration Targets
…
A set of views of a plane (not covered today)

## Slide 11: Camera Calibration Targets
A single, huge plane. What’s this for?

## Slide 12: Direct linear calibration
Solve for Projection Matrix P using least-squares (just like last class)
Advantages:
  All specifics of the camera summarized in one matrix
  Can predict where any world point will map to in the image
Disadvantages:
  Doesn’t tell us about particular parameters
  Mixes up internal and external parameters
    pose specific: move the camera and everything breaks

## Slide 13: Typical Perspective Model
focal length
principal point (image coords of camera origin on retina)
Just moves camera origin
2D Projection of X
rotation
translation
3D point

## Slide 14: Camera Calibration
Pairs of [X,Y,Z] and [u,v] → eqns to constrain M
How do I get [X,Y,Z], [u,v]?

## Slide 15: Stereo

## Slide 17: Amount of horizontal movement is …
…inversely proportional to the distance from the camera

## Slide 18: Depth from Stereo
Goal: recover depth by finding image coordinate x’ that corresponds to x
f
x
x’
Baseline B
z
C
C’
X
f
X
x
x'

## Slide 19: Depth from disparity
f
x’
Baseline B
z
O
O’
X
f
Disparity is inversely proportional to depth.
x

## Slide 20: Depth from Stereo
Goal: recover depth by finding image coordinate x’ that corresponds to x
Sub-Problems
  Calibration: How do we recover the relation of the cameras (if not already known)?
  Correspondence: How do we search for the matching point x’?
X
x
x'

## Slide 21: Correspondence Problem
We have two images taken from cameras with different intrinsic and extrinsic parameters
How do we match a point in the first image to a point in the second? How can we constrain our search?
x
?

## Slide 22: Key idea: Epipolar constraint
Potential matches for x have to lie on the corresponding line l’.
Potential matches for x’ have to lie on the corresponding line l.
x
x’
X
x’
X
x’
X

## Slide 23: Epipolar geometry: notation
Epipolar Plane – plane containing baseline (1D family)
Epipoles
= intersections of baseline with image planes
= projections of the other camera center
Baseline – line connecting the two camera centers
X
x
x’

## Slide 24: Epipolar geometry: notation
Epipolar Lines - intersections of epipolar plane with image planes (always come in corresponding pairs)
X
x
x’
Epipolar Plane – plane containing baseline (1D family)
Epipoles
= intersections of baseline with image planes
= projections of the other camera center
Baseline – line connecting the two camera centers

## Slide 25: Example: Converging cameras

## Slide 26: Example: Motion parallel to image plane

## Slide 27: Epipolar constraint
If we observe a point x in one image, where can the corresponding point x’ be in the other image?
x
x’
X

## Slide 28: Epipolar constraint
Potential matches for x have to lie on the corresponding
epipolar line l’.
Potential matches for x’ have to lie on the corresponding
epipolar line l.
x
x’
X
x’
X
x’
X

## Slide 29: Epipolar constraint example

## Slide 30: Epipolar constraint: Calibrated case
X
x
x’
Assume that the intrinsic and extrinsic parameters of the cameras are known
We can multiply the projection matrix of each camera (and the image points) by the inverse of the calibration matrix to get normalized image coordinates
We can also set the global coordinate system to the coordinate system of the first camera. Then the projection matrices of the two cameras can be written as [I | 0] and [R | t]

## Slide 31: Simplified Matrices for the 2 Cameras
= (R | T)

## Slide 32: Epipolar constraint: Calibrated case
X
x
x’ = Rx+t
R
t
The vectors Rx, t, and x’ are coplanar
= (x,1)T
Notes: X’ is X in the second camera’s coordinate system
We can identify the non-homogeneous 3D vectors X and X’ with the homogeneous coordinate vectors x and x’ of the projections of the two points into the two respective images

## Slide 33: Epipolar constraint: Calibrated case
Essential Matrix E
(Longuet-Higgins, 1981)
X
x
x’
The vectors Rx, t, and x’ are coplanar

## Slide 34: Epipolar constraint: Calibrated case
X
x
x’
E x is the epipolar line associated with x (l' = E x)
ETx' is the epipolar line associated with x' (l = ETx')
E e = 0 and ETe' = 0
E is singular (rank two)
E has five degrees of freedom

## Slide 35: Epipolar constraint: Uncalibrated case
X
x
x’
Fundamental Matrix
(Faugeras and Luong, 1992)

## Slide 36: Comparison of estimation algorithms
 | 8-point | Normalized 8-point | Nonlinear least squares
Av. Dist. 1 | 2.33 pixels | 0.92 pixel | 0.86 pixel
Av. Dist. 2 | 2.18 pixels | 0.85 pixel | 0.80 pixel

## Slide 37: Basic stereo matching algorithm
If necessary, rectify the two stereo images to transform epipolar lines into scanlines
For each pixel x in the first image
  Find corresponding epipolar scanline in the right image
  Search the scanline and pick the best match x’
  Compute disparity x-x’ and set depth(x) = fB/(x-x’)

## Slide 38: Basic stereo matching algorithm
For each pixel in the first image
  Find corresponding epipolar line in the right image
  Search along epipolar line and pick the best match
  Triangulate the matches to get depth information
Simplest case: epipolar lines are scanlines
  When does this happen?

## Slide 39: Stereo image rectification

## Slide 40: Stereo image rectification
Reproject image planes onto a common plane parallel to the line between camera centers
Pixel motion is horizontal after this transformation
Two homographies (3x3 transform), one for each input image reprojection
C. Loop and Z. Zhang. Computing Rectifying Homographies for Stereo Vision. IEEE Conf. Computer Vision and Pattern Recognition, 1999.

## Slide 41: Example
Unrectified
Rectified

## Slide 42
Matching cost
disparity
Left
Right
scanline
Slide a window along the right scanline and compare contents of that window with the reference window in the left image
Matching cost: SSD, SAD, or normalized correlation

## Slide 43: Correspondence search
Left
Right
scanline
SSD

## Slide 44: Correspondence search
Left
Right
scanline
Norm. corr

## Slide 45: Failures of correspondence search
Textureless surfaces
Occlusions, repetition
Non-Lambertian surfaces, specularities

## Slide 46: Results with window search
Window-based matching
Ground truth
Data

## Slide 47: Priors and constraints
Uniqueness
  For any point in one image, there should be at most one matching point in the other image
Ordering
  Corresponding points should be in the same order in both views
Smoothness
  We expect disparity values to change slowly (for the most part)

## Slide 48: Real-time stereo
Used for robot navigation (and other tasks)
  Several software-based real-time stereo techniques have been developed (most based on simple discrete search)
Nomad robot searches for meteorites in Antartica
  http://www.frc.ri.cmu.edu/projects/meteorobot/index.html

## Slide 49: Stereo reconstruction pipeline
  Camera calibration errors
  Poor image resolution
  Occlusions
  Violations of brightness constancy (specular reflections)
  Large motions
  Low-contrast image regions
Steps
  Calibrate cameras
  Rectify images
  Compute disparity
  Estimate depth
What will cause errors?

## Slide 50: Multi-view stereo ?

## Slide 51: Using more than two images
Multi-View Stereo for Community Photo Collections M. Goesele, N. Snavely, B. Curless, H. Hoppe, S. Seitz Proceedings of ICCV 2007,

## Slide 52: 1. Matlab 2. Current project.